## Slide 1: Making the Most of Uncertain Low-Level Measurements
Presented to the Savannah River Chapter of the Health Physics Society
Aiken, South Carolina, 2011 April 15
Daniel J. Strom, Kevin E. Joyce, Jay A. MacLellan, David J. Watson, Timothy P. Lynch, Cheryl. L. Antonio, Alan Birchall, Kevin K. Anderson, Peter A. Zharov
Pacific Northwest National Laboratory
strom@pnl.gov +1 509 375 2626
PNNL-SA-75679
Notes: Making the Most of Uncertain Low-Level Measurements
Strom DJ, KE Joyce, JA MacLellan, DJ Watson, TP Lynch, CL Antonio, A Birchall, and PA Zharov
Many measurement techniques in occupational and environmental monitoring produce results that have very substantial uncertainties. In many cases, a blank or background value must be subtracted from a gross result to produce a net result, a process that can produce non-physical, negative net results. When uncensored measurement results on a population are accompanied by well-characterized uncertainties, a novel method developed at PNNL separates the variance of the observations into two components, one arising from uncertainty and the other arising from population variability. Assuming the uncertain measurements are independent and unbiased, the method forces the arithmetic mean of the measurands (the “true values”) to equal that of the measurements. Further assuming that the measurands are lognormally distributed, the geometric mean and geometric standard deviation are calculated for a distribution of possibly true results. Assuming that the Bayesian prior probability density functions (PDF) of each individual measurement is a lognormal distribution comprised of every other measurand, posterior PDFs for each measurand are computed using Bayes’s theorem. The method corrects physically meaningless negative measurement results into PDFs of small positive values, but does little to alter large positive measurement results. Some surprising implications are illustrated by application to bioassay measurements of Sr-90, Cs-137, and Pu-239.
Abstract submitted to The 44th Annual Midyear Meeting of the Health Physics Society, Charleston, SC. PNNL-SA-75679.

## Slide 2: Prologue
Uncertainty is different for sets of sets of data than it is for single data points
If you have more than one uncertain measurement, you need to learn about measurement error models
HPs generally do not speak the language of statisticians well enough to be comprehended
  σ is not a synonym for standard deviation
  s is not σ is not
We have to get smarter!
  Or some biostatistician will commit regression calibration on our numbers!
Carroll RJ, D Ruppert, LA Stefanski, and CM Crainiceanu. 2006. Measurement Error in Nonlinear Models: A Modern Perspective. Chapman & Hall/CRC, Boca Raton.

## Slide 3: Outline
3
Censoring
The lognormal distribution
Measurements and measurands
Requirements and assumptions for this novel method
Population variability and measurement uncertainty
Disaggregating the variance
Distribution of measurands
The “everybody” prior

## Slide 4: Outline 2
4
Probability distributions for individual measurands
The Bayesian approach
The “everybody else” prior
Applications to real radiobioassay data
The importance of accurate uncertainty
Bohr’s correspondence principle
Conclusions

## Slide 5: Censoring
5
Changing a measurement result
Common practices
  Set negative values to 0
  Set all results less than some value to
    0
    ½ the value
    The value
    A non-numeric character like “M”
Changing measurement results causes great problems in statistical inference
  DR Helsel. 2005. Nondetects and data analysis. Statistics for censored environmental data. John Wiley & Sons.
This method requires uncensored data

## Slide 6: The Lognormal Distribution
6
Frequently observed in Nature
Multiplication of arbitrary distributions results in lognormals
  Ott WR. 1990. A Physical Explanation of the Lognormality of Pollutant Concentrations. J.Air Waste Mgt.Assoc. 40 (10):1378-1383

## Slide 7: Measurand, Measurement, Error, and Uncertainty (ISO)
7
measurand: particular quantity subject to measurement
  also, the “true value of the quantity subject to measurement”
result of a measurement: value attributed to a measurand, obtained by measurement
error: the unknown difference between the measurand and the measurement
  this is a different meaning from the theoretical concept in statistics!
uncertainty: a quantitative estimate of the magnitude of the error
  statisticians often do not distinguish between error and uncertainty and may use them synonymously

## Slide 8: Requirements and Assumptions
8
This method requires uncensored data
  small values are reported as they are calculated, with no rounding, setting negative values to zero, or otherwise changing
  Assume measurands are lognormally distributed
  Many populations in nature are lognormally distributed
  Lognormal common in radiological and environmental measurements
  Other functions could be used as long as they have a mean

## Slide 9: Population Variability and Measurement Uncertainty
9
The sample variance of a set of measurements on a population arises from two sources:
  population variability
  measurement error
If measurements have no error, then all observed sample variance is due to variability in the population

## Slide 10: Measurement Error Model
10
True values (measurands) ti give rise to measured values mi
We have good independent estimates of the combined standard uncertainty ui of each measurement mi
mi = ti + ui
ui ~ N(0, ui2)
We calculate the sample variance of mi
We use sample variance and a summary measure of the ui to estimate the variance due to population variability of ti

## Slide 11: Spread of Measurement Results (Sample Variance) Is Due to 2 Causes
Observed Spread
11
Variability within Population
“Average” Measurement Uncertainty

## Slide 12: Spread of Measurement Results (Sample Variance) Is Due to 2 Causes
12
Variability within Population
uRMS
Observed Spread

## Slide 13: Spread of Measurement Results (Sample Variance) Is Due to 2 Causes
13
uRMS
s(mi)
θ

## Slide 14: Estimating the Variance of the Distribution of Measurands
The “reliability” or “attenuation” or “variability fraction” is
Analogous to a correlation coefficient
  r2: fraction of variance explained by model
  r′ 2: fraction of variance due to measurand variability
Sample Variance
of the Measurements
Estimated Variance of the Measurands
Mean Square Measurement Uncertainty
☑ Known
☑ Known
☑ Calculated

## Slide 15: Distribution of Measurands
15
The estimated variance of the measurands is
Assume measurands are lognormally distributed
Assume the expectation of the measurands equals the mean of the measurements:
  measurements are unbiased
  this assumption respects the data
Calculate the parameters of the lognormal
  geometric mean
  geometric standard deviation sG
This is the distribution of “possibly true values”

## Slide 16: Analysis of Baseline Radiobioassay Data
16
90Sr: 128 baseline urine bioassays
  Everyone is exposed to global fallout
  gas proportional counter
  100-minute counts
137Cs: 5,337 baseline in vivo bioassays
  Everyone is exposed to global fallout & Chernobyl
  coaxial high-purity germanium (HPGe) scanning system
  10-minute scans
239+240Pu: 3,270 baseline urine bioassays
  All exposure is occupational; essentially no environmental exposure in North America
  α-spectrometry
  ~2,520 minute counts

## Slide 17
probability density
137Cs (mBq/kg)
239Pu (µBq/sample)
probability density
probability density
90Sr (mBq/day)
The “Everybody” Probability Density Function (PDF): A Distribution of Possibly True Values
Histogram and PDF have identical arithmetic means
Histogram of data
PDF of measurands

## Slide 18: Probability Distributions for Individual Measurands
18
Now that we have the lognormal PDF of all measurands, what can we say about individual measurands?
Each individual’s measurand is somewhere within the population of measurands
We now assume that each mi, ui pair is the mean and standard deviation of the Normal “likelihood” PDF for individual i
Assume the ith measurement was the last one made in the population
  When the ith measurement was made, the other M1 m and u values were known
Use this with Bayes’s theorem

## Slide 19: The Bayesian Approach to Assigning Possibly True Results to Individuals
19
Thomas Bayes 1702 – 1761

## Slide 20: Bayesian Method for Individuals
20
Instead of the “everybody” PDF, the “everybody else” PDF is used as the prior for each individual
Each individual’s likelihood is a normal distribution with mean mi and standard deviation ui
Using Bayes’s theorem, we developed a method to derive a posterior probability density function (PDF) for each individual’s measurand ti

## Slide 21: Applications to Real Radiobioassay Data
21
Impossible!
For Pu measurements, either the uncertainties ui are overestimated, or a covariance term has been neglected.
s(xi)

## Slide 22
137Cs
r´2=0.35
137Cs
Variability Fractions r′2

## Slide 23
90Sr
r´2=0.15
137Cs
r´2=0.35
90Sr
137Cs
Variability Fractions r′2

## Slide 24
239Pu
r´2~0
90Sr
r´2=0.15
137Cs
r´2=0.35
239Pu
90Sr
137Cs
Variability Fractions r′2

## Slide 25: 90Sr Results for 4 Individuals Uncensored Data Are Critical!
25
Measurement
Likelihood PDF
Prior
Measurand
Negative Result
Result ≈ Average
Result = Large Positive
Result ≈ 0

## Slide 26: A Movie of 128 90Sr Results
Short Dashes (Green): Likelihood (Data)
Long Dashes (Red): Everybody Else Prior
Solid (Blue): Posterior

## Slide 27
90Sr Measurands v Measurements

## Slide 28
90Sr Measurands v Measurements
Assigned Uncertainty

## Slide 29
29
29
Effect of Reducing Uncertainty
29
Assigned Uncertainty

## Slide 30
30
30
30
Effect of Reducing Uncertainty
30
Assigned Uncertainty

## Slide 31
31
31
31
31
Effect of Reducing Uncertainty
31
Assigned Uncertainty

## Slide 32
32
32
32
32
Effect of Reducing Uncertainty
32
Assigned Uncertainty

## Slide 33
33
33
33
33
33
Effect of Reducing Uncertainty
33
Assigned Uncertainty

## Slide 34
‹
uRMS
σ(νi)
Visualizing Uncertainty Reduction
r´2 = 0.15

## Slide 35
‹
uRMS
σ(νi)
Visualizing Uncertainty Reduction
r´2 = 0.15
r´2 = 0.57

## Slide 36
‹
uRMS
σ(νi)
Visualizing Uncertainty Reduction
r´2 = 0.15
r´2 = 0.57
r´2 = 0.78

## Slide 37
‹
uRMS
σ(νi)
Visualizing Uncertainty Reduction
r´2 = 0.15
r´2 = 0.57
r´2 = 0.78
r´2 = 0.94

## Slide 38
‹
uRMS
σ(νi)
r´2 = 0.15
Visualizing Uncertainty Reduction
r´2 = 0.57
r´2 = 0.78
r´2 = 0.94
r´2 ≈ 0

## Slide 39
The Common View:
The Measurement Is the Measurand
Oops! Activity < 0 is meaningless.
Oh, no! Results are
below some level
(DL, DT, LOD, etc.).
Might not be real!
Tilt

## Slide 40
The Bayesian View: The Measurement
and the Prior Give the Measurand

## Slide 41
The Bayesian View: The Measurement
and the Prior Give the Measurand

## Slide 64
The Bayesian View: The Measurement
and the Prior Give the Measurand

## Slide 65
5,337 137Cs Measurements Showing Uncertainty in Measurements & Measurands

## Slide 66
Assigned Uncertainty
5,337 137Cs Results with Same Uncertainty

## Slide 67
Assigned Uncertainty
5,331 137Cs Results

## Slide 68: The Importance of Accurate Uncertainty
68
Nearly the same measurement result
s(lower) ≈ 2.5s(upper)
Upper posterior resembles likelihood (i.e., measurement)
Lower posterior resembles prior
Upper (red) point
Lower (yellow) point
everybody else prior
likelihood (data)
posterior (measurand)
everybody else prior
likelihood (data)
posterior (measurand)

## Slide 69
5,331 137Cs Results

## Slide 70
Assigned Uncertainty
5,331 137Cs Results – Log Scale

## Slide 71: Innovation 1
71
this work addresses the situation in which each measurement is accompanied by a very good estimate of its uncertainty
  not described in the literature reviewed
  which occurs routinely in radiochemical and radiobioassay measurements

## Slide 72: Innovation 2
72
This work provides a solution to the vexing problem of making sense of negative measurement results for a quantity, such as activity in becquerels, which physically must be nonnegative
  none of the literature addresses negative values
The method makes sense of uncertain low-level measurements
  without injecting a bias into the dataset by left-censoring
  by implicitly recognizing that spurious negative results are accompanied by an equal amount of spurious positive signal

## Slide 73: Innovation 3
73
This work provides posterior estimates, in the form of probability distributions, of the true value of each measurand
  while the literature is concerned with correcting estimates of slopes of dose-response relationships for the effects of classical measurement error

## Slide 74: Innovation 4
74
This work shows that accurate estimates of uncertainty are as important as the values of the measurement results
  overestimates of uncertainty can lead to nonsense results

## Slide 75: Innovation 5
75
This work provides the ability to explore the impact of the magnitude of uncertainty on the posterior distribution of measurands by thought experiments involving substitution of the mean square measurement uncertainty, or some multiple or submultiple of it, for the individual uncertainties

## Slide 76: Innovation 6
76
The method is shown to closely correspond to classical (frequentist) methods when uncertainty is relatively small

## Slide 77: Innovation 7
77
This work answers the questions, conditional on plausible assumptions,
  “What true state of nature gave rise to this set of observations?”
  “For each individual measurement result, what are the probable values of the measurand that led to this measurement result?”
The authors believe that the method represents a significant step forward in the making sense of groups of uncertain, low-level radioactivity measurements

## Slide 78: Conclusions
78
Sample variance of a set of measurements is disaggregated into
  measurement uncertainty
  population variability
A reasonable, possible distribution of measurands for a population is the result
When , positive posterior PDFs of the measurand are computed using “everybody else” priors for each individual
  negative values are eliminated
  mean of measurements is preserved
When there is essentially no variance in the data due to population variability, the method cannot be expected to work, and it does not work

## Slide 79: Conclusions: Utility and Correspondence
79
The method eliminates negative measurement results in an uncensored data set and preserves the arithmetic mean of the data set
  If measurement results have a relatively large uncertainty, the posterior PDF of the measurand resembles the prior
  If the measurement results have a relatively small uncertainty, the posterior PDF of the measurand resembles the likelihood, that is, it is relatively close to the measurement result before application of the Bayesian methods
Best estimate of uncertainty is just as important as measurement!
As required by Bohr’s correspondence principle, results produced by the methods introduced here correspond to results of traditional statistical inference in the domain in which that inference is known to be correct

## Slide 80: Authors
Strom MacLellan Joyce Watson Lynch Antonio Zharov Birchall
(Mayak PA) (UK HPA) (Scherpelz, Vasilenko)
Acknowledgments
PNNL: Kevin Anderson, Gene Carbaugh, Michelle Johnson, Bruce Napier, Bob Scherpelz, Paul Stansbury, Rick Traub
SUBI: Vadim Vostrotin